## Slide 1
Nadi
On-device heart health + workout tracking • Android • No cloud
Camera rPPG + Hexagon NPU • Sensor-only workouts • 100% on-device privacy Reference: iQOO 15 • Snapdragon 8 Elite Gen 5 (SM8850) • devansh0703

## Slide 2
Two Dashboards, Zero Cloud
Heart • Workout
• HEART — contactless HR + stress from front camera (rPPG), INT8 1D-CNN on Hexagon NPU
• WORKOUT — rep counting + cardio, NO camera: accelerometer + GPS only
• Independent tabs; deny camera, workouts still work
• No frames, motion samples, or location traces leave the phone

## Slide 3
Heart Dashboard — How It Works
Camera → ROI → DSP → NPU → UI
• 30 FPS CameraX + MediaPipe Face Landmarker → forehead + cheek ROI
• Zero-alloc green-channel sampling (no GC pauses)
• Native C++: 300-sample buffer, Neon SIMD, Hamming, KissFFT → 0.75–3.0 Hz (45–180 BPM)
• SNPE INT8 DLC removes motion artifacts on Hexagon HTP
• Live HR, HRV stress, waveform, signal quality, on-device history

## Slide 4
Workout Dashboard — No Camera
Accelerometer ~33 Hz • GPS • Calibrate first
• Auto reps: push-ups, sit-ups, squats, jumping jacks (FitTrack hysteresis)
• Barbell: deadlift, overhead press, bench (RepCapture lift detector)
• Elliptical: manual timed mode — reports only elapsed time
• Running: distance (haversine), pace, 5000-pt route + cadence; AI run auto-start/pause

## Slide 5
Tech Stack
Compose • SNPE/DLC/HTP • Neon + FFT
• UI: Jetpack Compose M3, MVVM + StateFlow
• CameraX 1.3.0 • MediaPipe tasks-vision 0.10.0 • commons-math3
• Native: C++17, arm_neon, KissFFT • AI: SNPE DLC on Hexagon HTP (NPU-or-nothing)
• arm64-v8a only, API 26+, compiles SDK 36

## Slide 6
Device Gating + Privacy
On-device by architecture
• Workout runs anywhere the APK installs
• Heart gated to iQOO 15 (isSnapdragon8850), else unsupported screen
• PulseML needs DLC + SNPE AAR + Hexagon NPU; no CPU/GPU fallback
• Camera only for Heart; location only at run start

## Slide 7
Build & Use
Clone → Build → Install → Measure
• Needs: Studio Hedgehog+, NDK + CMake 3.22.1, SNPE AAR in app/libs/
• ./gradlew :app:assembleDebug → adb install -r app-debug.apk
• Heart: grant camera → center face → hold still → live HR + stress
• Workout: pick exercise → carry hint → calibrate → count → history (last 20)

## Slide 8
Thank You
Questions?
• Nadi — contactless heart + sensor workouts, fully on-device
• iQOO 15 • Snapdragon 8 Elite Gen 5 • Hexagon HTP v81
• github.com/devansh0703/Nadi • Arm AI Developer Challenge